## Slide 1: 5.3 Accommodation and Environmental Conditions
(ISO/IEC 17025:2005, Clause 5.3)
Nirmela Arsem
12 September 2018

## Slide 2: 5.3.1
5.3.1 Laboratory facilities for testing and/or calibration, including but not limited to energy sources, lighting and environmental conditions, shall be such as to facilitate correct performance of the tests and/or calibrations. The laboratory shall ensure that the environmental conditions do not invalidate the results or adversely affect the required quality of any measurement. Particular care shall be taken when sampling and tests and/or calibrations are undertaken at sites other than a permanent laboratory facility. The technical requirements for accommodation and environmental conditions that can affect the results of tests and calibrations shall be documented.
Identify sources and conditions that impact the test adversely
  Lighting
  Energy sources
  Dust
  Disinfection
  VOCs
Tests performed outside the lab
Document the technical requirements

## Slide 3: 5.3.2
5.3.2 The laboratory shall monitor, control and record environmental conditions as required by the relevant specifications, methods and procedures or where they influence the quality of the results. Due attention shall be paid, for example, to biological sterility, dust, electromagnetic disturbances, radiation, humidity, electrical supply, temperature, and sound and vibration levels, as appropriate to the technical activities concerned. Tests and calibrations shall be stopped when the environmental conditions jeopardize the results of the tests and/or calibrations.
Logbook for recording environmental conditions
Set limits for environmental conditions at which point testing will stop

## Slide 4: 5.3.3
5.3.3 There shall be effective separation between neighbouring areas in which there are incompatible activities. Measures shall be taken to prevent cross-contamination.
Identify sources of cross contamination
How to prevent cross contamination?

## Slide 5: 5.3.4
5.3.4 Access to and use of areas affecting the quality of the tests and/or calibrations shall be controlled. The laboratory shall determine the extent of control based on its particular circumstances.
Controlled access

## Slide 6: 5.3.5
5.3.5 Measures shall be taken to ensure good housekeeping in the laboratory. Special procedures shall be prepared where necessary.
Basic housekeeping
Additional housekeeping measures for special areas
Procedure for housekeeping