## Slide 1: Chlorine Residual Basin Plan Amendment Status and Issues
Pardee Technical Seminar
10/26/2018
Tom Hall, EOA

## Slide 2: BPA Project Components
Delete 0.0 mg/L TRC instantaneous maximum limit
Add 1984 EPA chlorine AWQC to Basin Plan
Select WQBEL averaging period and calculation method
Select initial dilution for deepwater dischargers
Select calculation formula for TRC WQBELs
Evaluate magnitude and duration criteria for excursions
Evaluate use and derivation of RL(s)
Consider if/when/how to address bacterial WQBELs

## Slide 3: POTW TRC Excursions
Total Residual Chlorine (TRC) continuous monitoring
POTW current 0.0 mg/L inst. max. compliance approach
  POTWs report 24 every-hour-on-the-hour readings daily (MMPs)
  Per RWB/BACWA 2004 letter agreement
CIWQS query: 01/01/2010 – 12/31/2017 (8 years)
  32 reported Cl2 excursions
  2 POTWs w/6 excursions; 3 w/3; 2 w/2; 7 w/1
  Max concentration during each excursion event in CIWQS
Average concentration = 1.66 mg/L
Average duration = 29.4 minutes

## Slide 4
Chart: SF Bay POTWs 2010 - 2017 Chlorine Residual Concentration Exceedances - Cumulative Probability
| 1 | 10.82 | 0.13 | 1.61 | 1.2 | 0.1 | 0.47 | 0.9 | 6.45 | 1.25 | 5.3 | 0.27 | 0.2 | 3.7 | 2.5 | 0.2 | 0.3 | 1.8 | 0.08 | 0.41 | 1.4 | 1.53 | 0.82 | 1.4 | 0.24 | 0.4 | 0.45 | 2.2999999999999998 | 2.79 | 1.7 | 0.75 | 0.63
CDF | 0.38374 | 0.99998 | 0.24643 | 0.49117 | 0.4184 | 0.2422 | 0.29691 | 0.36674 | 0.98415 | 0.42718 | 0.94871 | 0.26664 | 0.25643 | 0.81991 | 0.64689 | 0.25643 | 0.27108 | 0.52514 | 0.23941 | 0.28766 | 0.45371 | 0.47687 | 0.35332 | 0.45371 | 0.26224 | 0.28614 | 0.29381 | 0.61304 | 0.69391 | 0.50727 | 0.34172 | 0.32219

## Slide 5
Chart: SF Bay POTWs 2010 - 2017 Chlorine Residual Duration Exceedances - Cumulative Probability
| 87 | 0.7 | 3 | 15 | 19 | 23 | 90 | 29 | 10 | 12 | 11 | 9 | 60 | 15 | 27 | 1 | 6 | 5 | 9 | 75 | 83 | 71 | 15
 | 0.96982 | 0.17495 | 0.19495 | 0.31965 | 0.36757 | 0.41765 | 0.97592 | 0.49508 | 0.26381 | 0.28554 | 0.27457 | 0.25327 | 0.84089 | 0.31965 | 0.4691 | 0.17748 | 0.22302 | 0.21342 | 0.25327 | 0.9315 | 0.95975 | 0.91256 | 0.31965

## Slide 6: Bisulfite Issues
Over-dosing required for consistent compliance
  Operators extremely conservative
  Greater concern for violations than chemical costs
  Amount of over-dosing unknown (20-30%?; 3-5 mg/L?)
  20% over-dosing reduction = ~$0.7 M/yr cost saving
Bay-wide about 3+ MG of sodium bisulfite used annually
Bay-wide annual (2017) total bisulfite costs about $3.5 M
BACWA to interview POTWs on excess-dosing protocols
Excess bisulfite creates oxygen demand in RW

## Slide 7: Proposed Chlorine WQOs
Reference EPA Ambient Water Quality Criteria (AWQC) for Chlorine - 1984 (EPA 440/5-84-030)
  “These criteria are intended to apply to situations of continuous exposure, whether or not concentrations are fluctuating or constant, …” (p. 2)
  “… saltwater aquatic organisms and their uses should not be affected unacceptably if the four-day average concentration does not exceed 7.5 ug/L more than once every 3 years on the average and if the one-hour average concentration does not exceed 13 ug/L more than once every 3 years on the average.” (p. 18)
Adopt same EPA AWQC as WQOs in BP

## Slide 8: BPA Approach for TRC
Similar to April 2010 BPA adopting WQO for Bacteria
Minor BP modifications to add EPA Enterococcus WQO
  Modified Tables 3-1 and 4-2; added new Table 4-2A
  Modified language in Section 4.5.5.1
  Extensive data analysis not needed for TRC
  Can follow same basic staff report organization
Follow Supplemental Environmental Document (SED) and CEQA checklist formats
RWB staff to provide annotated version of staff report

## Slide 9: Proposed Basin Plan Modifications
Add 1984 EPA Chlorine AWQC to Tables 3-3 and 3-4
  Saltwater: 13 ug/L 1-hour average; 7.5 ug/L 4-day average
  Freshwater: 19 ug/L 1-hour average; 11 ug/L 4-day average
  Add footnote to each table with reference to EPA 1984 AWQC
Delete 0.0 mg/L limit from Basin Plan Table 4-2
Modify Table 4-2A
  Change title to read “Effluent Limitations for Bacteriological Indicators and Total Residual Chlorine”
  Add new column for “1-Hour Average (ug/L)”
  Under Parameters column add “Total Residual Chlorine” with subheadings Marine 13 and Freshwater 19 in 1-hour avg column

## Slide 10: Implementation Plan Modification
Add the underlined sentence below to BP Chapter 4 Section 4.5.5.1 Limitations for Conventional Pollutants:
  “Table 4-2a also contains 1-hour average effluent limitations for total residual chlorine applicable to all treatment facilities that use chlorine for effluent disinfection.” The water quality-based effluent limitations in Table 4-2a may be adjusted to account for dilution in a manner consistent with procedures in the Policy for Implementation of Toxics Standards for Inland Surface Waters, Enclosed Bays, and Estuaries of California (see footnotes ‘a’ and ‘e’ in Table 4-2a.

## Slide 11: Deepwater POTW Initial Dilution
Actual dilution only used for deepwater discharger ammonia WQBELs
Current ammonia dilution values compiled by RWB
  Generally different dilutions used for acute and chronic calcs
  Acute values range from 3:1 (Calistoga) to 117:1 (WCA)
TRC non-conservative like ammonia and cyanide
  Dilution only WQBELs don’t account for decay, adsorption, etc.
Various models and assumptions used in dilution studies
  Simplest to use existing ammonia acute dilutions for TRC calcs
  POTWs may want to update old dilution studies

## Slide 12: TRC WQBEL Calculation
TRC not priority pollutant so not required to use SIP
SIP based priority pollutants limits expressed as
  Average monthly effluent limit (AMEL)
  Monthly average effluent limit (MDEL)
  No parameters now with 1-hour average limits
SIP section 1.4 effluent limit formula
  Ce = Co + Dm(Co – Cs)
  Ce=effluent limit, Co=WQO, Dm=dilution, Cs=background
Ocean Plan same same formula for TRC and bacteria

## Slide 13: Flows, Dilution, 1-hr Avg Limit
Discharger | Design Flow (mgd) | FY 17/18 Flow (mgd) | Acute Initial Dilution | TRC Limit (mg/L)
EBDA | 107.8 | 59.7 | 79:1 | 1.04
EBMUD | 120 | 52.5 | 25:1 | 0.34
SFPUC SE | 84.5 | 57.4 | 51:1 | 0.68
West County | 28.5 | 9.8 | 117:1 | 1.50
San Jose | 167 | 87.0 | 0 | 0.013
Sunnyvale | 29.5 | 10.6 | 0 | 0.013

## Slide 14: Averaging Period and Calculation
Need 24-times/day to derive 1-hour average values from continuous monitoring data recorded in SCADA system
SCADA polls and records TRC analyzer readings at intervals ranging from seconds to minutes
Multiple calculation options (no specified approach)
  Simple single every hour on hour reading?
  Arithmetic average (AA) calculations at least every 15 minutes
  AA calculations at least every 5 minutes (SWB 2008 recc.)
  AA based on total number of SCADA system readings per hour
Compare each hourly value to 1-hour average WQBEL

## Slide 15: Magnitude/Duration Criteria
Santa Ana RWB TRC compliance determination
  TRC WQO and effluent limit = 0.1 mg/L (inst. max)
  No individual excursion from 0.1 mg/L shall exceed 5 minutes
  No individual excursion shall exceed 5.0 mg/L
  Total excursions shall not exceed 7 hrs and 26 min per month (99% compliance)
Based on current pH approach per 40 CFR 404.17
  99% compliance per month
  No individual excursion shall exceed 60 minutes

## Slide 16: TRC Compliance Determination
Potential magnitude/duration criteria – examples
  Criteria apply to readings (e.g., 5-min x 12) in 1-hour avg calcs
  No individual excursion above WQBEL shall exceed XX minutes
  No individual excursion above WQBEL shall exceed YY mg/L
  Total excursions shall not exceed ZZ minutes per month
Complicated to calculate and report (program SCADA?)
May not be easily CIWQS compatible
Possibly at counter purposes to reducing bisulfite use

## Slide 17: Current Bacterial Limits
Basin Plan Implementation Plans Section 4.5.5.1
  References bacterial WQBELs in Table 4-2A
  Enterococcus WQO 35 MPN/100 mL (geometric mean)
  WQBELs in Table 4-2A may be adjusted for dilution
Most NPDES permit bacterial limits
  Set equal to WQOs (no dilution)
  Enterococcus WQBEL = 35 MPN/100 mL
EBDA permit one of few with WQBELs
  Actual dilution 79:1 but only 10:1 used
  Enterococcus WQBEL = 240 MPN/100 mL

## Slide 18: Benefits of Bacterial WQBELs
Current limits extremely conservative
  Bacteria subject to inactivation, die-off, etc. in RW
  Limited fully body immersion contact recreation near outfalls
Dilution based bacterial WQBELs
  Allows for reduced chlorine and bisulfite dosages
  Still fully protective of REC-1 beneficial uses
  Need rationale for backsliding exception(s)
SWB adopted new bacterial WQOs (08/07/2018)
  Enterococcus lowered from 35 to 30 MPN/100 mL
  New 100 MPN/100 mL E. coli (freshwater only)
  Need Table 4-2A and implementation updates for conformity

## Slide 19: Shallow Water Dischargers
Shallow water discharger effluent limits
  Zero dilution credit allowed except for cyanide WQBELs
  Basin Plan Table 4-6 allows 3.0:1 to 4.0:1 cyanide dilution credits
  If assume 3.0:1 dilution for TRC; WQBEL = ~0.04 mg/L
  Limited benefits over current 0.0 mg/L limit (1-hour averaging)
Alternative compliance approaches under investigation
  TRC reporting limits (RL) possible to include in NPDES permits
  Most TRC RLs in CA for handheld field instruments (0.1 mg/L)
  Most RLs for drinking water (SWB Order WQ 2014-0194-DWQ)
  RL use uncertain for continuous vs grab sample TRC monitoring

## Slide 20: Discussion Items
General approach reasonable?
1-hour averaging period calculation preferences?
Are RLs needed for deepwater compliance evaluations?
  SCADA system directly reads/records/averages all values
  Most TRC WQBELs in ~0.3 – 1.0 mg/L range
Level of investigation needed on shallow water RLs?
Include part or all of SWB Bacterial WQOs in this BPA?
Availability of RWB staff to work on BPA?
Other items