## Slide 1
Pretreatment Program Basics
BACWA/EBMUD Pretreatment Training
March 11, 2019
Greg V. Arthur - (510) 967-8411 - gva@gvarthur.com

## Slide 2
Pretreatment Program Basics
Clean Water Act applied to indirect non-domestic discharges
EPA
DOJ
State Water
State AGs
DAs
Sewer Districts
Municipals
JPAs
Counties
treatment unit to remove metals at a metal finisher

## Slide 3
40 CFR 403.2
Purpose and Objectives
Prevent
interference
Prevent
pass-through
Improve
reclaim/recycle
wastewater
and sludges
reaction end-point monitoring for metals precip, Cr-reduction, CN-destruction

## Slide 4
40 CFR 403.3
Pretreatment Program Definitions
POTW – publicly-owned treatment works
Industrial User (IU) – non-domestic indirect discharger
Interference – discharge that causes or contributes to a
treatment works inhibition, resulting in a violation by POTW
Pass-Through – discharge of pollutants that passes through
a treatment works, resulting in a violation by the POTW
New Source – new facility or replacement of existing facility
Significant Industrial User (SIU) – IU determined to be high
flow (25k gpd), high load (5%), high risk, or categorical
Approval Authority – State or EPA approves PT Programs

## Slide 5
40 CFR 403.4
State and Local Law
The Federal
pretreatment
rules do not
preclude States
or local govern-
ments from
establishing
additional and
more stringent
law
final settling tank following aerobic bioreactors at a surfactant manufacturer

## Slide 6
40 CFR 403.5
National Prohibitions and Local Limits
General Prohibitions
pass-through or interference
Specific Prohibitions
fire or explosion hazards (flashpoint <140°F)
causing corrosive structural damage to treatment works
solids or viscous pollutants causing obstructions
oxygen demanding pollutants which will cause interference
heat which will inhibit biological activity (<104°F influent)

## Slide 7
40 CFR 403.5
National Prohibitions and Local Limits
Specific Prohibitions
petroleum and non-biodegradable oils that will cause
interference or pass-through
trucked or hauled wastes except at designated points
Local Limits
numerical expression of general and specific prohibitions
technically-based treatment works MAHLs
defensible allocations and/or BMPs to IUs
enacted through local sewer use ordinance

## Slide 8
40 CFR 403.5
National Prohibitions and Local Limits
Municipal Local Limits

## Slide 9
40 CFR 403.5
National Prohibitions and Local Limits
Municipal Local Limits

## Slide 10
40 CFR 403.5
National Prohibitions / Local Limits
Municipal Local Limits
official permitted sample point

## Slide 11
40 CFR 403.6
Technology-based Categorical Standards
Sections 407-471 Effluent Guidelines
compliance deadlines
concentration to flow-based mass limits
production-based mass to concentration limits
prohibition against dilution as a substitute for treatment
combined wastestream formula
definition of regulated, unregulated, and dilution waters
end-of-process-after-treatment sampling

## Slide 12
40 CFR 403.6
Technology-based Categorical Standards
Sections 407-471 Effluent Guidelines
combined wastestream formula
40 CFR 403.6(e)
Qtotal - Qdilution - Qunregulated
Ctotal = x
Qtotal
regulated – defined categorical wastestreams
dilution – boiler blowdown, non-contact cooling, storm
water, demineralizer backwash, domestic wastewater and
Appendix D subcategory wastewaters
unregulated – everything else

## Slide 13
40 CFR 403.6
Technology-based Categorical Standards
Pharmaceuticals 40 CFR 437
applicability
regulated pollutants
basis of standards
new vs existing source
dilution as sub for treatment
combined wastestream formula
sampling locations
compliance deadline

## Slide 14
40 CFR 403.6
Technology-based Categorical Standards
end of process after treatment

## Slide 15
40 CFR 403.7 and 403.11
Removal Credits for Categorical Standards
Sections 407-471 Effluent Guidelines
Alternate Federal
standards based
on treatment
plants removals
None in Region 9
ever approved by
EPA or States
activated sludge aeration raceways at a municipal sewage treatment plant

## Slide 16
40 CFR 403.8
POTW Pretreatment Program Requirements
8(a) – POTWs with WWTPs total design flow > 5 mgd
8(b) – Administered to ensure compliance by IUs
8(f)1 – Legal authority (including MJPA)
issue permits (duration, non-transferability, effluent limits,
self-monitoring, penalties, slug discharge control)
conduct inspections and monitoring to determine com-
pliance independent of information supplied by the IUs
obtain injunctive relief, and civil and criminal penalties
halt or prevent discharges which pose or may pose immi-
nent endangerment to health, welfare, envr, or POTW

## Slide 17
40 CFR 403.8
POTW Pretreatment Program Requirements
8(f)2 – Implement Procedures
compile inventory of IUs and identify the character and
volume of pollutants discharged
notify IUs of requirements and SIUs of their status
receive and analyze self-monitoring
inspect and sample to obtain results independent of
information from the IUs (at least once per year for SIUs)
require slug control plans
investigate non-compliance
publish annually the SIUs in significant non-compliance

## Slide 18
40 CFR 403.8
POTW Pretreatment Program Requirements
8(f)3 – Funding
sufficient re-
sources and
qualified person-
nel to enact the
legal authority
and implement
the procedures
8(f)4 – Local Limits
develop local
limits
batch treatment for chromium reduction, metals precipitation, settling

## Slide 19
40 CFR 403.8
POTW Pretreatment Program Requirements
8(f)5 – ERP
implement
an enforcement
response plan
SUO Checklist
8(f)6 – SIU List
maintain and
submit list of SIUs
industrial wastewater treatment unit for toxic metals and acids at a plating shop

## Slide 20
40 CFR 403.9 and 403.18
Pretreatment Program Approval and Modification
9(b) – Contents
of POTW Program
Submittal
certifying state-
ment of legal
authority
local limits
IU inventory
permitting
monitoring
ERP
rotating-drum electrowinning silver recovery for movie film processing plant

## Slide 21
40 CFR 403.10
State Pretreatment Programs
10(e) – State PT
Program in lieu of
POTW Programs
Connecticut
Vermont
Alabama
Mississippi
Nebraska
chem-aided de-emulsion oil water separator unit for oily ships bilge waters

## Slide 22
40 CFR 403.12
Monitoring and Reporting for POTWs and IUs
12(b) – CIU Baseline Monitoring Reports
12(d) – CIU 90-day Compliance Report
12(e) – CIU Periodic Compliance Reports
self-monitoring at least twice per year
self-certification in lieu of sampling for pollutants not
present, if waived by permit
12(h) – SIU Periodic Compliance Reports
self-monitoring at least twice per year
12(f) – Notification of potential slug load discharges

## Slide 23
40 CFR 403.12
Monitoring and Reporting for POTWs and IUs
12(g) – Monitoring and Analysis for CIUs, SIUs, POTWs
monitoring by the POTW in lieu of self-monitoring
24-hour notification upon becoming aware of a violation
resample in 30 days of becoming aware of a violation
sample record representative over the reporting period
samples representative the sampling period
grab samples for pH, CN, S=, phenols, VOAs as also
defined in Appendix E
24-hour composite sampling for all other pollutants
analyses in accordance with 40 CFR 136
more frequent self-monitoring must be reported

## Slide 24
40 CFR 403.12
Monitoring and Reporting for POTWs and IUs
12(i) – POTW Annual Report
updated IU inventory
summary of IU compliance status
summary of enforcement activities
summary of changes to the POTW Pretreatment Program
12(j) – IU Notification of substantial changes in discharge
12(l) – IU Signatory Requirements
12(m) – POTW Signatory Requirements

## Slide 25
40 CFR 403.12
Monitoring and Reporting for POTWs and IUs
12(o) – POTW and IU Record-keeping requirements
updated IU inventory
summary of IU compliance status
summary of enforcement activities
summary of changes to the POTW Pretreatment Program
12(p) – IU notification of discharges that would otherwise be
hazardous waste under 40 CFR 261
Domestic Sewage Exclusion
DTSC Permit-by-Rule
12(r) – Electronic reporting in 40 CFR 3

## Slide 26
40 CFR 403.13
Fundamental Different Factors
Case by Case
Variance of
Categorical Stds
CIU request 180
days after pub-
lication date of
categorical std
Not Applicable
vibratory deburring silt catchment prior to discharge to the sewers

## Slide 27
40 CFR 403.14
Confidentiality
IU Submittals
No – production
data to determine
limits
No – effluent or
flow data
Maybe – All other
data claimed as
“confidential”
under 40 CFR 2
No – Any data
not claimed
oily drainage skimming and equalization for tank farm flows

## Slide 28
40 CFR 403.15
Net/Gross Calculations
Adjustment of
categorical stds
to account for
intake water
Intake from same
water body that
the POTW dis-
charges into
Treatment would
meet standards
without intake
concentrations
portable pump and hose delivery at a metal finishing shop

## Slide 29
40 CFR 403.16
Upset Provision
Affirmative
defense for IU
violations
Entirely outside
of IU’s control
unworkable sample point with too many contributing discharges

## Slide 30
40 CFR 403.17
Bypass Provision
17(d) – Prohibi-
tion against the
bypassing of
treatment neces-
sary to comply
Unless …
no feasible
alternative
unavoidable to
prevent loss of
life, injury, or
severe damage.
final effluent flume flow meter

## Slide 31
Pretreatment Program Basics
BACWA/EBMUD Pretreatment Training
March 11, 2019
Questions or Comments
Greg V. Arthur - (510) 967-8411 - gva@gvarthur.com